## Slide 1: Juniper cloud labs EVPN DCI use case
Victor Ganjian
WW POC Engineer
December 2014
Cloud Labs
Notes: Welcome to the Juniper Cloud Labs Ethernet VPN Data Center Interconnect Use Case.
In this video I will step you through the Use Case to help you prepare for your customer demo.

## Slide 2: BEFORE STARTING – Ixia setup
There are some steps that need to be performed on the Ixia in preparation for the demonstration
  Start IxNetwork GUI – open the config file for this use case
  Resolve ARP
    Navigate to Protocols  Protocol Interfaces
    Select all ports and then click “Send ARP” at top of window
    When ARPs are resolved ‘Port Link’ state is ‘green’, without red ‘!’
  Apply Configured Traffic Items
    Navigate to TrafficL2-3 Traffic Items
    Select the pull down arrow on the “L2-3 Traffic” icon at top left
    Select “Apply L2-3 Traffic”
  Set up Stats Window
    The bottom half of the main window is for stats
    At top of Stats area click “Select Views…”
    Select “Traffic Item Statistics” and click “OK”
Delete this slide before presenting to customer
Notes: Once the EVPN DCI Topology has been reserved in JCL, you will need to prepare the IxNetwork application for the Use Case.
The IxNetwork configuration consists of 3 Tester Ports that are connected to different points in the use case topology. Each Tester Port emulates one or more IP hosts.
The first step is to make sure that each host can resolve ARP for its configured default gateway. To do this …..
Next, apply the pre-configure traffic items that will be used to generate traffic during the use case……..
The last step is to configure the Statistics window so that it will properly display the Traffic Item statistics during the demo………

## Slide 3: Before starting – physical topology
The physical topology of the JCL setup is shown above
Understanding Tester Port 1 (TP1) Connectivity
  It is connected to ge-0/0/0 of CE10
  The VLAN membership of port ge-0/0/0 determine which Data Center TP1 is connected to
  Initially ge-0/0/0 is a member of VLAN 100, so TP1 is connected to PE11/PE12 in DC1
  During the demonstration TP1 is logically moved to DC2 by changing the VLAN membership of the access port to VLAN 2 which connects it, via ge-0/0/1, to PE21 port xe-0/0/0.
Note the logical topology diagram contains a “CE20” switch, but this switch does not exist, it is logical
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3 (Ixia 4/11)
31.1.1.2/24
Remote Site
ESI 11:12
TP1 (Ixia 4/1)
100.1.1.10
0x10
DG: .1
V100
TP2 (Ixia 4/12)
100.1.1.20-.23
0x64:01:01:20-23
DG: .2
xe-0/0/0
xe-0/0/3
xe-0/0/0
xe-0/0/1
xe-0/0/3
xe-0/0/2
xe-0/0/1
xe-2/0/0
xe-2/0/2
xe-2/0/1
xe-2/0/3
xe-0/0/1
ge-0/0/0
ge-1/0/1
ge-0/0/2
ge-0/0/3
ge-0/0/1
untagged access
V2
Delete this slide before presenting to customer
Notes: This slide shows the physical topology of the EVPN DCI Use Case.
The topology includes 3 different locations, Data Center 1, Data Center 2, and a Remote Site. Each site has either 1 or 2 Provider Edge routers.
Note that Tester Port 1 is connected to an access port on a layer 2 edge switch CE10. The VLAN membership of this access port determines which Data Center the Tester Port 1 host is connected to. Initially Tester Port 1 is a member of VLAN 100 which connects to PE11 and PE12 in Data Center 1. During the demonstration Tester Port 1 is logically moved to Data Center 2 by changing the VLAN membership of this access port to VLAN 2.
The logical topology diagrams display a CE20 switch at Data Center 2. However, note that CE20 is not a separate physical switch, it is a logical switch.

## Slide 4: BEFORE STARTING – notes
Refer to the notes pages for instructions on how to execute some of the steps on the slide
  Commands corresponding to CLI configuration changes on CE10
  Notes to help assist with navigating Ixia IxNetwork GUI
Please familiarize yourself with this demo by going through it a few times before presenting to your customer
Delete this slide before presenting to customer
Notes: If, during the demonstration, you are not sure about how to start a traffic flow or what CLI commands to enter, just check the notes pages for instructions.
In general it is a good idea to run through the demo a few times on your own before presenting to your customer.

## Slide 5: EVPN DCI Solution overview
Motivation
  Seamless interconnect for DCI – L3 aware L2 stretch between DCs
  Seamless workload migration - VM mobility across DCs
  Wide Applicability – Interconnects Native L2 and overlay DC technologies like VXLAN, MPLS in DC
EVPN is a standards based Layer 2 VPN solution that addresses the requirements for the Data Center Interconnectivity (DCI) application
  Its MP-BGP Control Plane supports:
    Optimization of traffic paths for flows between mobile hosts in the Data Center and remote sites/Internet
    Multi-homing configuration for load-balancing and resiliency
    Inter-subnet routing
    Efficient MAC learning and MAC Mobility
    Application of policy to control MAC route advertisements
    Flexible use of data plane technologies – MPLS, GRE, VXLAN
Juniper is leading this technology in the IETF standards body and in software implementation
Notes: The main application of EVPN is Data Center Interconnect which provides seamless layer 2 interconnectivity between Data Centers over a Layer 3 core network. A driver for this type of connectivity is seamless workload migration, or the ability to move Virtual machines between Data Centers to improve application performance, improve server resource utilization, and maintain high availability of applications. EVPN is essentially a layer 2 VPN service and that provides connectivity regardless of what type of Data Center technology is used at each site.
EVPN is a standards based solution that addresses specific requirements for the Data Center Interconnectivity application. What is unique about EVPN, as compared to VPLS and other L2 forwarding solutions, is that MAC learning occurs in the control plane. This enables a set of features that addresses the requirements for DCI including optimization of traffic paths to and from mobile hosts in the Data Center, Multi-homing for load balancing and resiliency, and seamless integration of layer 3 routing.
Juniper is co-author of the EVPN IETF standard and offers an advanced feature set in its software implementation across multiple products.

## Slide 6: agenda
Use Case Network Topology – review high level configuration
EVPN Instance (EVI) configuration review
Multi-homing
  Configuration
  Designated Forwarder
  Aliasing – load balancing of traffic
Layer 3 Forwarding
    Configuration
    Default Gateway Synchronization
    IP/MAC Synchronization
Notes: The Agenda for the EVPN DCI Use Case is as follows….
First, we will review the network topology and then look at a simple EVPN instance configuration.
Then we’ll focus in on some of the key attributes of EVPN including multi-homing, traffic load balancing also known as Aliasing, and seamless integration of layer 3 routing. In the latter section we will focus on the optimization of the forwarding paths taken by traffic flows to and from a host as it moves between Data Centers.

## Slide 7: Topology elements
MX router
  PE router
Routing Instances
  Either EVPN Instance (EVI) or IPVPN running on PE
Layer 2 Ethernet Switch
  CE Device
Tester Port
  For generating traffic
EVI1
VPN1
Notes: As a reference, here are some of the icons used in the topology diagrams throughout this demonstration.

## Slide 8: Topology
Core
  Each PE has MP-IBGP session to Route Reflector PE31 (family evpn & inet-vpn). Single AS 65000.
  Single OSPF Area with full mesh of RSVP-TE LSPs between PEs.
  PE31 only configured for IPVPN membership (no EVPN)
DC
  CE10 – layer 2 switch, LAG to 2 PEs (no LACP) in DC1.
  PE11 and PE12 – common Ethernet Segment Identifier (ESI) in “all-active” mode
  – access interface in VLAN 100 in EVPN Instance (EVI1), type VLAN Base service
  - VLAN 100 IRB in IPVPN (VPN1) configured as 100.1.1.1/24 with MAC 0x64:01:01:01
  PE21 – configured for same EVI/IPVPN. VLAN 100 IRB configured as 100.1.1.2/24 with MAC 0x64:01:01:02
Hosts
  Tester ports on EVPN VLAN in DC1 and DC2. Tester port at Remote Site. Note IPs and MACs.
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3
31.1.1.2/24
Remote Site
ESI 11:12
TP1
100.1.1.10
0x10
DG: .1
V100
CE20
TP2
100.1.1.20-.23
0x64:01:01:20-23
DG: .2
Notes: Each site in the topology has either 1 or 2 PE routers which communicate with each other over an IP Core.
All core facing interfaces on the PE routers are configured with OSPF.
A full mesh of RSVP-TE signaled Label Switched Paths are established between all PE routers.
Multi Protocol BGP is used to exchange reachability information of the EVPN and IPVPN instances configured on the PE routers.
In Data Center 1 there are two PE routers configured for Multi-Homing. A layer 2 switch, CE10, is configured with a LAG whose members terminate on PE11 and PE12. A single VLAN, VLAN 100, spans all of the devices and is mapped to the EVPN-1 instance on the PEs. Also, an IRB interface is defined on the VLAN on both PE11 and PE12 with an address of 100.1.1.1 and is used as the default gateway by the host TP1, or Tester Port 1, connected to CE10. The IRB interface is placed into the IPVPN-1 instance for routing.
The configuration of the PE router in Data Center 2 is similar. There, PE21 is configured with an EVPN-1 instance and the VLAN IRB interface has an IP address of 100.1.1.2 which is used as the default gateway by the 4 hosts emulated by TP2, or Tester Port 2. This IRB interface is also placed into the local IPVPN-1 instance.
At the Remote site is a single PE router named PE31. It is configured with only the IPVPN-1 instance. Tester Port 3 is connected directly to PE31 and will be used to send and receive traffic to host TP1 at the Data Center.
Since EVPN is a layer 2 VPN service please make note of the IP and MAC address information of the hosts. The most important one to remember is TP1 with IP address 100.1.1.10 and MAC address of Hex “10”.

## Slide 9: EVPN Instance (EVI) Configuration
In this Use Case the VLAN Base Service Interface is used
  Single VLAN per EVI
  “instance-type” is “evpn”, contains VLAN Id, and access interface(s)
  jcladmin@PE11> show configuration
  <snip>
  routing-instances {
  EVPN-1 {
  instance-type evpn;
  vlan-id 100;
  interface xe-0/0/0.100;
  routing-interface irb.100;
  route-distinguisher 11.11.11.11:1;
  vrf-target target:100:1;
  protocols {
  evpn;
  }
  }
  }
Also supported is the VLAN Aware Bundle Service Interface
  Multiple VLANs per EVI, each with its own forwarding table
  “instance-type” is “virtual-switch”
Notes: Currently the Juniper MX supports two types of EVPN Service Interfaces. The first is the VLAN Base Service Interface where there is a 1 to 1 relationship between VLAN and EVPN Instance. This is the service interface used in this demonstration as seen in the Routing Instance configuration for EVPN-1. Note that the “instance-type” is “evpn”.
The other option is the VLAN Aware Bundle Service interface where multiple VLANs are mapped to a single EVPN instance. Note that each VLAN maintains a separate layer 2 forwarding table in this case. When configuring an EVPN Instance with multiple VLANs the “instance-type” is set to “virtual-switch”.

## Slide 10: Multi-homing - Configuration
PE11 and PE12 configured with common Ethernet Segment Identifier (ESI)
  “all-active” means that both links between CE10 and multi-homed PEs are always active and can forward traffic.
  jcladmin@PE11> show configuration interfaces
  xe-0/0/0 {
  flexible-vlan-tagging;
  encapsulation flexible-ethernet-services;
  esi {
  11:12:11:12:11:12:11:12:11:12;
  all-active;
  }
  unit 100 {
  encapsulation vlan-bridge;
  vlan-id 100;
  }
  }
Notes: Multi-homing is a key feature for EVPN as it provides high availability in the event of a node or link failure and it also enables traffic load balancing as we will see shortly.
To configure multi-homing just set the Ethernet Segment Identifier on the access ports of the multiple PE routers to the same ESI value.
In this demonstration the multi-homing mode is set to “all active” because we want both uplinks from CE10 to both PE11 and PE12 to always carry traffic.

## Slide 11: Multi-homing – Designated forwarder
PE11 and PE12 automatically discover one another
  via MP-BGP Ethernet Segment advertisement that includes ESI
PE11 and PE12 elect a Designated Forwarder (DF)
  DF is responsible for forwarding BUM traffic from core to CE
  jcladmin@PE11> show evpn instance EVPN-1 extensive
  Instance: EVPN-1
  <snip>
  Number of ethernet segments: 1
  ESI: 11:12:11:12:11:12:11:12:11:12
  Status: Resolved by IFL xe-0/0/0.100
  Local interface: xe-0/0/0.100, Status: Up/Forwarding
  Number of remote PEs connected: 1
  Remote PE MAC label Aliasing label Mode
  12.12.12.12 299904 299904 all-active
  Designated forwarder: 11.11.11.11
  Backup forwarder: 12.12.12.12
  Advertised MAC label: 299840
  Advertised aliasing label: 299840
  Advertised split horizon label: 299856
Notes: Once Multi Homing is configured both PE11 and PE12 will automatically discover that they are connected to the same Ethernet Segment.
Each PE then runs the same algorithm to determine which one of them will be elected the Designated Forwarder. The Designated Forwarder is responsible for forwarding BUM traffic received from remote PEs towards the local CE device. The Backup Forwarder discards BUM traffic destined towards the local CE device. This prevents looping of layer 2 traffic.
In this case the CLI output on PE11 shows that PE11 is the designated forwarder.

## Slide 12: Multi-homing - Aliasing
EVPN Multi-homed connectivity is advertised by PE11 & PE12 to PE21
  Common Ethernet segment identified by ESI
Mode “all-active” enables PE21 to load balance traffic destined to hosts connected to the ESI, also known as Aliasing
  jcladmin@PE21> show evpn instance EVPN-1 extensive
  Instance: EVPN-1
  <snip>
  Number of ethernet segments: 1
  ESI: 11:12:11:12:11:12:11:12:11:12
  Status: Resolved by NH 1048579
  Number of remote PEs connected: 2
  Remote PE MAC label Aliasing label Mode
  11.11.11.11 299840 299840 all-active
  12.12.12.12 299904 299904 all-active
Notes: PE11 and PE12 also advertise their multi-homing topology to the remote PEs [via MP-BGP].
In this case PE21 learns that PE11 and PE12 are both connected to the same Ethernet Segment and that they are both able to forward traffic since the mode is ‘all-active’.
This enables PE21 to load balance traffic destined to that ethernet segment to both PE11 and PE12. This ability to load balance bridged or routed traffic is known as “Aliasing”.

## Slide 13: Multi-homing - Aliasing
EVPN Forwarding Table on PE21 has entry for TP1 (0x10) in Data Center 1
  MAC flag “C” – learned via MP-BGP EVPN MAC Route
  Next-Hop Index points to a list of LSPs to PE11 and PE12 which corresponds to the ESI on which the MAC was learned.
jcladmin@PE21> show evpn mac-table
MAC flags (S -static MAC, D -dynamic MAC, L -locally learned, C -Control MAC
O -OVSDB MAC, SE -Statistics enabled, NM -Non configured MAC, R -Remote PE MAC)
Routing instance : EVPN-1
Bridging domain : __EVPN-1__, VLAN : 100
MAC MAC Logical NH RTR
address flags interface Index ID
00:00:00:00:00:10 DC 1048579 1048579
00:00:64:01:01:20 D ge-1/0/1.100
Notes: To demonstrate Aliasing lets first check the layer 2 forwarding table on PE21.
As shown in the CLI output, PE21 has dynamically learned the MAC address of Tester Port 1, in this case “Hex 10”, via a Multi Protocol BGP MAC Advertisement Route update. This route update contains the ESI value corresponding to the multi-homed ethernet segment in Data Center 1. Therefore PE21 will forward traffic to this MAC destination to both PE11 and PE12.

## Slide 14: Multi-homing - Aliasing
From IxNetwork start 4 flows from 4 hosts on TP2 to 1 host on TP1
LSP statistics on PE21 show that traffic is load balanced to PE11 (3 flows) and PE12 (1 flow)
  jcladmin@PE21> clear mpls lsp statistics
  jcladmin@PE21> show mpls lsp statistics ingress
  Ingress LSP: 3 sessions
  To From State Packets Bytes LSPname
  11.11.11.11 21.21.21.21 Up 11931 3006618 from-21-to-11
  12.12.12.12 21.21.21.21 Up 3978 1002462 from-21-to-12
  31.31.31.31 21.21.21.21 Up 0 0 from-21-to-31
Stop Ixia flows when finished
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3
31.1.1.2/24
Remote Site
ESI 11:12
TP1
100.1.1.10
0x10
DG: .1
V100
CE20
TP2
100.1.1.20-.23
0x64:01:01:20-23
DG: .2
Traffic flows from DC2 to DC1 are load-balanced on LSPs to PE11 and PE12
Notes: IXIA INSTRUCTIONS
To start the Ixia flows in IxNetwork, navigate to Traffic L2-3 Traffic Items
Start the Traffic Item named “TP2  TP1 Aliasing” by clicking on the green “Play” button for the specific Traffic Item.
Do NOT click the main “Play” button at the top left of the IxNetwork window as this will start all streams.
Note: the Ixia may show that extra packets were received, denoted by an “*” in the “Loss %” statistic. As of 14.1R4 this is expected (PR 1043198). If this is a problem during the demo just stop and restart the Traffic Item.
Stop the Ixia flows before continuing to the next slide.
DEMO SCRIPT Lets start some traffic flows from the 4 emulated hosts on Tester Port 2 in Data Center 2 destined to Tester Port 1 in Data Center 1. In this case all hosts are in the same EVPN so traffic will be bridged.
The LSP statistics on PE21 show that traffic is load balanced to PE11 and PE12. It looks like 3 of the flows are forwarded to PE11 and 1 flow is forwarded to PE12.

## Slide 15: Layer 3 forwarding – configuration
An IRB interface for the EVPN VLAN is required for L3 forwarding
The IRB interface is associated with a common IPVPN
    jcladmin@PE11> show configuration routing-instances
    EVPN-1 {
    instance-type evpn;
    vlan-id 100;
    interface xe-0/0/0.100;
    routing-interface irb.100;
    route-distinguisher 11.11.11.11:1;
    vrf-target target:100:1;
    protocols {
    evpn;
    }
    }
    IPVPN-1 {
    instance-type vrf;
    interface irb.100;
    route-distinguisher 11.11.11.11:111;
    vrf-target target:100:101;
    vrf-table-label;
    }
Notes: One of the key attributes of EVPN is that it supports seamless integration of layer 3 forwarding.
To accomplish this an IRB interface is configured on the EVPN VLAN and then associated with an IPVPN routing instance.
In this demo interface irb.100 is defined for EVPN VLAN 100. This IRB interface is then placed into the IPVPN-1 routing instance.

## Slide 16: Layer 3 forwarding – Def GW Synchronization
The IRB interface is the default gateway for the hosts on the EVPN VLAN
The IRB IP-MAC binding is advertised to remote PEs to synchronize default gateway information
  A PE will Proxy-ARP and forward traffic on behalf of remote PE based on destination MAC address
Optimizes path of outbound traffic flows from DC to remote destinations
    jcladmin@PE11> show evpn peer-gateway-macs
    Routing instance : EVPN-1
    Bridging domain : __EVPN-1__, VLAN : 100
    Installed GW MAC addresses:
    00:00:64:01:01:02
    jcladmin@PE21> show evpn peer-gateway-macs
    Routing instance : EVPN-1
    Bridging domain : __EVPN-1__, VLAN : 100
    Installed GW MAC addresses:
    00:00:64:01:01:01
Notes: Remember that the IRB interface represents the default gateway for the hosts on the EVPN VLAN.
The IP-MAC address binding of the IRB interface is advertised to remote PEs to synchronize default gateway information. This enables a PE to proxy-ARP and forward traffic on behalf of a remote PE based, using the remote PE’s MAC address.
For example, the CLI output on PE21 shows that it will route packets that contain a destination MAC address corresponding to the configured IRB interface on PE11.
This feature is key to optimizing the forwarding path of outbound traffic flows from the Data Center.

## Slide 17: Layer 3 forwarding – Def GW Synchronization
From IxNetwork start traffic flows from host TP1 to host TP3 at the Remote Site
Traffic from the DC to a Remote Site is routed using the IPVPN forwarding table
  TP1 is configured to use IRB/Default Gateway in DC1
  On PE11 and PE12 the route to TP3 (31.1.1/24) is via LSP to PE31
  jcladmin@PE11> show route 31.1.1.2 table IPVPN-1.inet.0
  IPVPN-1.inet.0: 6 destinations, 10 routes (6 active, 0 holddown, 4 hidden)
  + = Active Route, - = Last Active, * = Both
  31.1.1.0/24 *[BGP/170] 03:41:17, localpref 100, from 31.31.31.31
  AS path: I, validation-state: unverified
  > to 10.11.31.31 via xe-0/0/1.0, label-switched-path from-11-to-31
  jcladmin@PE12> show route 31.1.1.2 table IPVPN-1.inet.0
  IPVPN-1.inet.0: 6 destinations, 9 routes (6 active, 0 holddown, 3 hidden)
  + = Active Route, - = Last Active, * = Both
  31.1.1.0/24 *[BGP/170] 03:52:38, localpref 100, from 31.31.31.31
  AS path: I, validation-state: unverified
  > to 10.12.31.31 via xe-0/0/1.0, label-switched-path from-12-to-31
Notes:   IXIA INSTRUCTIONS
  If the traffic flows from the previous test are still running please stop them now.
  In IxNetwork start the Traffic Item named “TP1  TP3 Remote” by clicking on the green “Play” button for the specific Traffic Item.
  Do NOT click the main “Play” button at the top left of the IxNetwork window as this will start all streams.
DEMO SCRIPT
To demonstrate default gateway synchronization, lets start a traffic flow from Tester Port 1 in Data Center 1 to Tester Port 3 at the Remote Site.
Tester Port 1 is configured to use 100.1.1.1 as the default gateway which matches the IRB interface configuration on PE11 and PE12.
To reach the destination 31.1.1.2 at the Remote Site, the IPVPN forwarding tables on both PE11 and PE12 will forward traffic to PE31.

## Slide 18: Layer 3 forwarding – Def GW Synchronization
Check LSP statistics on PE11 or PE12 (depending on where flow is hashed) to verify that traffic is sent directly to PE31.
  jcladmin@PE12> clear mpls lsp statistics
  jcladmin@PE12> show mpls lsp statistics ingress
  Ingress LSP: 3 sessions
  To From State Packets Bytes LSPname
  11.11.11.11 12.12.12.12 Up 0 0 from-12-to-11
  21.21.21.21 12.12.12.12 Up 0 0 from-12-to-21
  31.31.31.31 12.12.12.12 Up 1989 473382 from-12-to-31
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3
31.1.1.2/24
Remote Site
ESI 11:12
TP1
100.1.1.10
0x10
DG: .1
V100
CE20
Notes: Depending on how CE10 hashes the flow, either PE11 or PE12 will receive the flow and forward it to PE31. In this case PE12 receives the traffic flow. This can be verified by viewing the MPLS LSP statistics on PE12.

## Slide 19: Layer 3 forwarding – Def GW Synchronization
By making some configuration changes in the topology, TP1 is moved to the access interface on PE21.
This simulates a host moving from DC1 to DC2 (ex. VMotion).
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3
31.1.1.2/24
Remote Site
ESI 11:12
TP1
100.1.1.10
0x10
DG: .1
V100
CE20
Notes: CLI INSTRUCTIONS
Execute the commands below on CE10 to simulate TP1 moving from DC1 to DC2. Note that all that is being done here is changing the VLAN membership of the access port TP1 is connected to. On CE10 VLAN 2 connects to PE21 port xe-0/0/0.
    delete interfaces ge-0/0/0.0 family ethernet-switching vlan members 100
    set interfaces ge-0/0/0.0 family ethernet-switching vlan members 2
    commit
    OR
    edit interfaces ge-0/0/0.0 family ethernet-switching vlan
    delete members 100
    set members 2
    commit
DEMO SCRIPT
Now lets simulate the moving of the Tester Port 1 host from Data Center 1 to Data Center 2, similar to a Vmware VMotion. This is done by modifying the configuration on CE10 as mentioned previously.

## Slide 20: Layer 3 forwarding – Def GW Synchronization
Because PE21 has synchronized Default Gateway info from PE11/PE12 it routes the traffic itself
Check statistics on PE21 to verify that traffic is sent directly to PE31 and NOT back to DC1.
  jcladmin@PE21> clear mpls lsp statistics
  jcladmin@PE21> show mpls lsp statistics ingress
  Ingress LSP: 3 sessions
  To From State Packets Bytes LSPname
  11.11.11.11 21.21.21.21 Up 0 0 from-21-to-11
  12.12.12.12 21.21.21.21 Up 0 0 from-21-to-12
  31.31.31.31 21.21.21.21 Up 3977 946526 from-21-to-31
Stop the Traffic Item before continuing
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3
31.1.1.2/24
Remote Site
ESI 11:12
TP1
100.1.1.10
0x10
DG: .1
V100
CE20
Even after TP1 moves to DC2, traffic to the Remote Site continues to take most direct, optimal path
Recall TP1 is configured with Def GW 100.1.1.1 which matches PEs in DC1
Notes: Now the Tester Port 1 host is in Data Center 2. We can see from the MPLS LSP statistics on PE21 that PE21 is forwarding the traffic directly to PE31.
This confirms that traffic from the Data Center continues to take the most direct path to the Remote Site.
Even though PE21 is configured with a different IRB IP address, it still acts as a default gateway for the Tester Port 1 host.
IXIA INSTRUCTIONS – Stop the traffic flow before continuing

## Slide 21: Layer 3 forwarding – IP-MAC Synchronization
IP-MAC Synchronization optimizes path of inbound traffic flows from remote sources to DC destinations
PE learns host MAC-IP bindings by snooping ARP packets
  Advertises binding in EVPN
  jcladmin@PE21> show evpn database
  Instance: EVPN-1
  VLAN MAC address Active source Timestamp IP address
  100 00:00:00:00:00:10 xe-0/0/0.0 Nov 18 21:53:40 100.1.1.10
  100 00:00:64:01:01:01 11.11.11.11 Nov 18 16:42:05 100.1.1.1
  100 00:00:64:01:01:02 irb.100 Nov 18 16:42:09 100.1.1.2
  100 00:00:64:01:01:20 ge-1/0/1.100 Nov 18 21:56:51 100.1.1.20
Notes: We’ve now seen how traffic flows from the Data Center take the most direct path to the remote site. But what about traffic flows inbound towards the Data Center? EVPN optimizes these flows as well using IP-MAC synchronization.
When an EVPN PE learns of a host’s IP-MAC binding it shares this information with remote EVPN peers by sending a BGP MAC Advertisement route. The IP-MAC binding is learned originally by the PE by snooping the information contained in received ARP Packets.
The IP-MAC bindings can be viewed using the “show evpn database” command.

## Slide 22: Layer 3 forwarding – IP-MAC Synchronization
  If EVPN VLAN is configured with IRB interface then a corresponding host route is installed in IPVPN VRF
Forwarding table on PE31 for destination TP1 (100.1.1.10) has next-hop PE21
  Host route was advertised by PE21 to all IPVPN member PEs
jcladmin@PE31> show route 100.1.1.10 table IPVPN-1.inet.0
IPVPN-1.inet.0: 5 destinations, 7 routes (5 active, 0 holddown, 0 hidden)
+ = Active Route, - = Last Active, * = Both
100.1.1.10/32 *[BGP/170] 21:06:08, localpref 100, from 21.21.21.21
AS path: I, validation-state: unverified
> to 10.21.31.21 via xe-2/0/2.0, label-switched-path from-31-to-21
Notes:   DEMO SCRIPT
  If the EVPN VLAN is configured with an IRB interface then a host route corresponding to the IP-MAC binding is is installed in the IPVPN route table. This host route is advertised to all members of the IPVPN including PE31 at the Remote Site.
  In this case, the CLI output on PE31 shows that the Tester Port 1 host 100.1.1.10 is reachable via PE21.

## Slide 23: Layer 3 forwarding – IP-MAC Synchronization
  From IxNetwork start traffic flow from host TP3 at the remote site to host TP1
Check statistics on PE31 to verify that traffic is sent directly to PE21
  jcladmin@PE31> clear mpls lsp statistics
  jcladmin@PE31> show mpls lsp statistics ingress
  Ingress LSP: 3 sessions
  To From State Packets Bytes LSPname
  11.11.11.11 31.31.31.31 Up 0 0 from-31-to-11
  12.12.12.12 31.31.31.31 Up 0 0 from-31-to-12
  21.21.21.21 31.31.31.31 Up 3977 946526 from-31-to-21
Stop the Ixia flow before continuing
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3
31.1.1.2/24
Remote Site
ESI 11:12
TP1
100.1.1.10
0x10
DG: .1
V100
CE20
Notes:   IXIA INSTRUCTIONS
  In IxNetwork start Traffic Item named “TP3 Remote  TP1”
  Optionally verify that packets are received by TP1 - view “Traffic Item Statistics” in IxNetwork Statistics window
  DEMO SCRIPT
  From the Ixia start a traffic flow from Tester Port 3 at the Remote Site to the Tester Port 1 host at Data Center 2.
  The MPLS LSP statistics on PE31 confirm that traffic is sent directly to PE21.

## Slide 24: Layer 3 forwarding – IP-MAC Synchronization
By making some configuration changes in the topology TP1 is moved to DC1
This connects TP1 to the access Ethernet segment shared by PE11/PE12, simulating a host moving from DC2 to DC1 (i.e. VMotion).
From IxNetwork send an ARP Request from TP1 to simulate a Gratuitous ARP
  During VMWare VMotion the virtual host issues a GARP so that forwarding tables are updated
  This causes PE11/PE12 to send an updated host route to PE31
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3
31.1.1.2/24
Remote Site
ESI 11:12
TP1
100.1.1.10
0x10
DG: .1
V100
CE20
Notes: CLI INSTRUCTIONS
Execute the commands below on CE10 to simulate TP1 moving from DC1 to DC2. Note that all that is being done here is changing the VLAN membership of the access port TP1 is connected to. On CE10 VLAN 2 connects to PE21 port xe-0/0/0.
    delete interfaces ge-0/0/0.0 family ethernet-switching vlan members 2
    set interfaces ge-0/0/0.0 family ethernet-switching vlan members 100
    commit
    OR
    rollback 1
    commit and
  To send ARP on Ixia navigate to ProtocolsProtocol Interfaces. Then select the row for “TP1” and click “Send ARP” at the top of the window.
DEMO SCRIPT
Now lets simulate the moving of the Tester Port 1 host from Data Center 2 to Data Center 1, similar to a Vmware Vmotion event. This is done by modifying the configuration on CE10.
After the host is moved we need to transmit an ARP packet which is required in order for PE11 and PE12 to send an updated host route to PE31.
This simulates the behavior of an actual Virtual Machine host, which transmit a Gratuitous ARP after it has been moved to the target server.

## Slide 25: Layer 3 forwarding – IP-MAC Synchronization
Restart the Ixia traffic flow from TP3 to TP1
PE31 now forwards traffic destined to TP1 (100.1.1.10) directly to DC1
  jcladmin@PE31> show route 100.1.1.10 table IPVPN-1.inet.0
  IPVPN-1.inet.0: 5 destinations, 7 routes (5 active, 0 holddown, 0 hidden)
  + = Active Route, - = Last Active, * = Both
  100.1.1.10/32 *[BGP/170] 00:00:48, localpref 100, from 11.11.11.11
  AS path: I, validation-state: unverified
  > to 10.11.31.11 via xe-2/0/1.0, label-switched-path from-31-to-11
Check LSP statistics on PE31.
CE10
PE11
PE12
PE31
PE21
IP/MPLS Core
with MP-BGP
DC1
DC2
EVI1
VPN1
EVI1
VPN1
EVI1
VPN1
VPN1
V100
TP3
31.1.1.2/24
Remote Site
ESI 11:12
V100
CE20
Even after host TP1 moves to DC1, traffic from the Remote Site continues to take most direct, optimal path
TP1
100.1.1.10
0x10
DG: .1
Notes: When the traffic flow is restarted we can see from the MPLS LSP statistics on PE31 that the flow is forwarded to a PE in Data Center 1.
This confirms that traffic from the Remote Site continues to take the most direct path to the destination host, even after it has moved.
FINAL STEP - When finished stop the Ixia traffic flow.

## Slide 26: Key Takeaways
Multi-homing
Default Gateway Synchronization
IP-MAC Synchronization
Ease of Provisioning
Active/Active links enables Aliasing (Load Balancing)
Optimal outbound routing from hosts in DC to remote locations
Optimal inbound routing from remote locations to DC hosts
Integrates with existing Services running over IP Core networks. Only EVI and ESI configuration is new.
Notes: In conclusion lets summarize some of the key features that we have covered in this Use Case.
First, we reviewed the all active Multi-Homing configuration and demonstrated that a remote PE can load balance traffic to both of the PEs connected to the multi-homed ethernet segment.
For Default Gateway Synchronization and IP-MAC Synchronization we demonstrated how the traffic flows were forwarded along the most optimal paths, even when a host was moved from one Data Center to another.
Finally, another point to emphasize is the ease of provisioning EVPN. We reviewed the EVPN routing instance configuration and note here that it can be easily integrated into an existing network that supports other VPN services such as VPLS or IPVPN since it uses Multi Protocol BGP in the control plane. We also mentioned the Designated Forwarding election process and Aliasing feature which take place automatically and do not require any special configuration.

## Slide 27
Q & A

## Slide 28: For more information
Juniper Day One Guide – Building Dynamic Overlay Service-Aware Networks
http://www.juniper.net/us/en/training/jnbooks/day-one/juniper-validated-solutions/building-dynamic-overlay/
IETF L2 VPN Standards - BGP MPLS Based Ethernet VPN
https://datatracker.ietf.org/wg/l2vpn/documents/
Juniper Technical Publications - EVPN Overview
http://www.juniper.net/documentation/en_US/junos14.2/topics/concept/evpns-overview.html

## Slide 29
Juniper Cloud Labs
Bringing Solutions to Life
Notes: 29
This concludes the overview of the EVPN DCI Use Case. I hope this has helped you get a better understanding of the Use Case and will help you with your presentation to your customer. Thank you.